###### MCE to complete shaded area:

| MCE Job Number: | Date Received: |
| --- | --- |
| Job Name: | Job Engineer: |

Job Type

Federal Government	 DoD / UFGS	 Other Government

School or University	    (TSSA Cert. Req’d)	 State Government

Hospital 	 Office Building	 Courthouse	 Jail / Prison	 Other        	 Private

Site & Contact Information

Site Address

Owner Representative

Print Name:

Signature:

Title:

Business Phone:

Cell Phone:

eMail:

Address:

Contractor Information

Business Name:

Contact Name:

Business Phone:

Cell Phone:

eMail:

Address:

Consultant Information

Business Name:

Contact Name:

Business Phone:

Cell Phone:

eMail:

Address:

Form Completed By

Name:

Business Phone:

Cell Phone:

eMail:

Address:

Shipping Information

| Ship to Address: |  |
| --- | --- |
| Notice Required: | 24 hrs | 48 hrs |
| Lift Gate Truck Required: | Yes | No |

Logistics Information (continued)

Delivery & Payment Schedule

Standard MCE terms of payment (net 30 days) apply to your order. If you require special terms of payment, please provide an Alternative Payment Schedule.

# Per state tax laws, it is critical that MCE receive exemption or resale certificates prior to the material being shipped and billed. If the job is a tax-exempt job, send the exemption certificate with this form. If you are a resale customer and have a resale certificate, please make sure that the MCE accounting department has a copy on file.

| Customer Job Number: |  |
| --- | --- |
| Customer PO Number: |  |
| Job Name: |  |
| Number of cars: |  |
| Control | Delivery Date | Payment Date |
| Car “ ” |  |  |
| Car “ ” |  |  |
| Car “ ” |  |  |
| Car “ ” |  |  |
| Car “ ” |  |  |
| Car “ ” |  |  |
| Group “ ” |  |  |

Delivery & Payment Schedule

If different payment terms are required, please provide an alternative proposal. Please include specifics of building owner payments and provide a copy of your contract.

Alternative Proposal Provided:  	  Yes    	 No

Contract Attached:                     	  Yes    	 No

# Job Push-Outs and Cancellation

Jobs pushed out by the customer more than 90 days beyond the originally scheduled date may be subject to cancellation charges as follows:

*     Before engineering commences: 10% of total sales order

*     After engineering completed:       30% of total sales order

*     After construction completed:      75% of total sales order

Extra Documentation

If this job requires additional engineering drawing packages or additional manuals, please indicate below.

| Drawing Sets | # Required: |
| --- | --- |
| Manuals | # Required: |

# Elevator Safety Code Compliance

Accurate information is essential. Both hardware and software are affected.

| Job Location (City/State): |
| --- |
| Contract Date: |
| Project Type: | New Construction | Modernization |
| Elevator Duty: | Passenger | Service | Freight |
| Measurements: | U.S./Imperial | S.I./Metric |
| North American Compliance: | U.S. | Canada |
| ASME A17.1/B44 Edition: 2019 |
| 2016 | 2013 | 2010 | 2007 | 2004 | 2000 |
| Addenda/Supplements: (None for A17.1-2010 and later) | 2008(a) | 2005(a) | 2002(a) |
|  | 2009(b) | 2005(S) | 2003(b) |
| ASME A17.1-1996/98 |
| ASME A17.1- (Specify edition & addenda) |
| International compliance: |
| Australia AS 1735 |
| EN 81 |
| Other (Specify): |
| Additional jurisdictional code compliance: |
| California medical facility OSHPD Seismic Certification (additional charge for certified cabinet) |
| Chicago Fire Code (select one): Current OR 2001 |
| Denver | Pressurized hoistway |
| GSA |
| Hawaii |
| Houston, TX | Existing Door Reopen Button, Fire Phase I |
| Maryland |
| Massachusetts |
| Michigan | Permit/contract date prior to 6/21/2010? |
| Nebraska |
| New York City, NY | Appendix K | RS-18 |
| Seattle, Washington | Multiple Phase I Switches |
| Washington State | # of 3-position: | # of 2-position: sws: |
| TSSA | Collapsible Car Top Guard Rail |
| UFGS Specs Specify Branch: |
| Additional Compliance Requirements? Explain: |
| Job Specification |
| Does project have job specifications? Yes No If yes, number of pages: Have specifications been forwarded to MCE? Yes No |

| Type of Operation |
| --- |
| Simplex |
| Parking Floor: | Floor Label: |
| If no parking floor, car stays at last call answered. |
| Selective collective (intermediate floors have two call buttons in hall) |
| SAPB Single Automatic Pushbutton (intermediate floors have one call button in hall) |
| SBC Single Button Collective (intermediate floors have one call button in hall) |
| Duplex or Group (provide hoistway and machine room drawings) |
| Duplex Selective Collective Group Operation Number of hall call risers per floor: First Parking Floor: Floor Label: Second Parking Floor: Floor Label: Third Parking Floor: Floor Label: First free car will park at First Parking floor. Second free car will park at Second Parking floor, etc. If no parking floors, cars stay at last call answered floor. |
| Swing Car Operation Car(s): Please describe in special instructions on next page. |
| Cross Cancellation Panel (existing must be relay logic) (Existing hall P/B schematics are required.) |
| Cross Registration (Existing hall P/B schematics are required.) |
| Fire Service Operation |
| Fire Service Phase I |
| Main Landing #: Floor Label: Doors will open: Front Rear |
| Alternate Landing #: Floor Label: Doors will open: Front Rear NOTE: For flood hazard zones, the designated and alternate fire recall floors should be at or above the base flood elevation. |
| Additional Fire Phase I main return switch: Switch location: Landing #: Floor Label: |
| Hoistway smoke detectors At or below lower level of recall Above lower level of recall |
| “Elevator Control Panel” (Chicago “high rise” only) |
| Fire Service Phase II Fire Service Access Elevator(s)? (list) |
| Additional Fire Operation Requirements for Detroit MI, or GSA/Federal Jurisdictions: Shunt Trip Delay Heat Detectors: ( MR HW Each floor ) |

# Operating Features

| Attendant Service Annunciator Panel in car |
| --- |
| Car-to-Lobby Lobby/Floor switch Location: Car Hall Remote Panel |
| Park with doors: Open Closed (not recommended if in-car switch) |
| Return Landing#: | Floor Label: |
| Earthquake Service (shuts car down at floor) |
| Emergency Medical Technician Service (EMT) |
| Landing #: | Floor label: |

# Operating Features (continued)

| Emergency Power Generator: (not battery lowering) Generator voltage same as line voltage? Yes No Does same generator power other cars? Yes No Number of cars to run at a time: 1 2 3 : |
| --- |
| Emer pwr contacts during normal pwr: Open Closed |
| Power pre-transfer contact – 10 sec minimum |
| Manual Select Switch Number of positions: Labels: Is emergency/standby power selector switch located at the designated level in view of all elevator entrances? Yes No |
| Fan / Light Timer Option (Turns off in-car fan and light after period of inactivity) |
| Flood Operation Lowest landing that the car can go in an event of a flood: Landing: ___ Floor Label: _____ NOTE: The designated and alternate fire recall floors should be at or above this level. |
| Foldable/Collapsible Cartop Rail |
| Hospital Service (Code Blue): |
| Landing #s: | Floor labels: |
| Independent Service Pre-test switch in Controller |
| Sabbath Operation |
| Inspection/Access Requirements |
| Car Top Inspection Station Yes No by MCE (NEMA 1 only) |
| Extended Shaft Car Top Inspection Yes No (Bypasses 1st set of directional limits to move the car further up the hoistway during car top inspection; 2nd set of directional limits required, along with a separate multi-pole switch on car top complying with A17.1, 2.26.4.3; both sets of directional limits must be physical switches.) |
| Hoistway Access Operation | Yes | No |
| Top access switch: | Yes | No |
| Switch location: | Front | Rear |
| Bottom access switch: | Yes | No |
| Switch location: | Front | Rear |
| Select In-car Access (enable) switch type below. |
| In-Car Inspection Operation Yes No Using top/bottom car calls or up/down buttons. Select In-car Inspection switch type below |
| In-Car Inspection and/or Access Switch type (Only for ASME A17.1-2000/CSA B44-00 or later) 2-Position Inspection (INSP/NORM) switch 2-Position Access (ENABLE/OFF) switch 3-Position (INSP/OFF/ACCESS ENABLE) switch |
| Load Weighing Yes No (Discrete oil pressure switches for load weighing) |
| Monitoring |
| mView complete in machine room mView interface only to allow future connection |
| iMonitor / iReport, machine room or remote iMon/Report interface only to allow future connection |
| IDS Liftnet interface |
| Security |
| Car Call Security Card reader lockouts (dry contacts) Car call card reader override switch Switch Location: Keyed floor lockout switches Switch location: Car Hall: Number of switches: Floor Lockouts via PC (iMonitor) Basic security (enter security code using car call buttons) Enable/disable via: Key-switch on/off ¦ Location: 7-Day Timer (hardware) Hall Call Security Card reader lockouts (dry contacts Hall call card reader override switch Single switch overrides all car and hall card readers. Location: Keyed floor lockout switches) Floor Lockouts via PC (iMonitor) |
| Bypass Security: (Fire service bypass is standard) Independent Service Attendant Service Other: |
| Enclosures |
| Machine room NEMA rating: 1(std) 12 4 4X Number of machine rooms: Air-conditioned enclosure (recommended for all but NEMA 1) Hinged enclosure (additional charge) GFCI outlet required in enclosure (added charge) Light required in enclosure (added charge) Enclosure pedestals required 2 inch 12 inch (Not available for OSHPD jobs) Machine room space limitations? Indicate maximum space available for enclosure. Otherwise, MCE will select the enclosure based on job requirements. (Consider also limitations of entry halls and doors.) H x W x D |
| Line Voltage |
| (actual measured line voltage) Choose closest below. 600 575 480 460 440 415 380 240 230 220 208 200 115 Other: |
| AC 3 Phase (standard) AC 2 Phase AC Single Phase AC 3 phase (grounded leg delta configuration)* * ATL motor starting only, unless isolation transformer used. |
| 60 Hz (standard in U.S.) 50 Hz |
| Available Fault Current from AC Feed (kA): Standard Controller SCCR (Short Circuit Current Rating): Up to 50 hp: 5kA 51-200 hp: 10kA If the available fault current exceeds these standard values, please notify MCE for a quote. |
| Other Power Related Features Brown Out Circuit TVSS Surge Suppressor |

Motor Starting

(All MCE starters include Reverse Phase Sensor)

Solid State 3/9 Lead Motor 6/12 Lead Motor (standard)

WYE-DELTA

ATL (Across the Line)

Customer supplied starter (Interface charges apply. Indicate type of starter above.) Brand: Model: Remote In MCE controller MCE to install (customer shipping to MCE) Customer to install (provide location/dimension sketch) Additional charges will apply if coil voltage other than 120VAC.

Hydraulic Data

Pump Motor(s)

New by MCE (Complete pump unit data form) New Existing

HP: Motor brand:

Full load amps (MCE will estimate if blank):

Starts per hour: 80 (std) 120 (requires larger starter)

Multiple Motors (complete only for 2 or more motors) Number of motors: 2 3 4 Number of disconnects: 1 2 3 4 Starting: Sequential (recommended) Simultaneous Single motor operation if abnormal conditions

# Valve(s)

Brand Maxton Blain EECO TKE/Dover Bucher (Beringer) Other (specify): Model:

Number of valves: 1 (standard) 2 3 4

Coils per valve: 1 2 3 4 (standard) 5

Voltage: 120VAC (standard) Other (additional charge): V=

# Hydraulic Features

Battery Powered Lowering By MCE Other: (electrical schematic required)

Life Jacket Interface

Low Oil Switch

Oil Tank Temperature Shutdown Switch

Pressure Switch Interface (required when top of cylinder is above top of storage tank)

Resynchronous circuit for telescopic or dual pistons

Roped Hydro Governor Set (electrical schematic required) Governor Set/Reset Coil Voltage:

Viscosity Control

Door Information

Car Gate

Automatic passenger style doors Powered freight style doors Manual doors Other:

Gate Release Solenoid (not standard) Yes No

Voltage: 3-Phase AC 1-Phase AC DC Fuse: 2A 3A Other:

Hoistway Doors

Automatic passenger style doors Powered freight style doors Manual doors (complete below) Other: (complete below) Interlocks: Closed contact Yes No Locked contact Yes No Door locking cam Retiring (not driven by automatic passenger style car gate) Voltage: 3-Ph AC 1-Ph AC DC Fuse: 2A 3A Other: Fixed cam Bar lock (manually operated) Mechnical (Driven by automatic passenger style car gate)

Door Features

Infrared detector unit/photo eye Cut-out switch in COP Anti-Nuisance

Mechanical safety edge

Heavy doors at landings (list landings):

Dual door operators on same side for wide opening

Cartop door open/close buttons (nonsolid state door operators)

Door Hold Operation (non-fire operation) Switch Button (max hold = 120 seconds)

Nudging Reduced torque with buzzer Buzzer only Ignore photo eye after seconds If safety edge or door open button activated, doors should: Stop Re-open Other:

Sketch or Special Instructions

| Automatic Passenger Style Doors |
| --- |
| MCE |
| SmarTraq Complete (Complete SmarTraq data forms) |
| SmarTraq Upgrade (Upgrades existing operator to closed loop. Mark existing model below.) |
| GAL |
| MOVFR I |  |
| MOVFR II | Voltage: 220VAC 110VAC (220 is default if no selection made) |
| MOMVC/MOHVC | MOM/MOH |
| MOD (230V) | MOSVCL |
| MOD (115V) | MOPM-P/MOPM-PL |
| MODHA | MOCT/MOCTA/MODCT/ MOMCT/MOHCT |
| MODVC/MODHVC | Motor Voltage: | 220 | 110 |
| MOA | Logic Voltage: | 220 | 110 |
| MAC/Kone |
| PM-SSC/104 Board | MAC (old style) |
| AMD/Kone |  |
| TKE/Dover |
| HD03M | HDLM |
| HD68/70/73/91 |  |
| HD98/85 (Requires SmarTraq upgrade kit) |
| Otis |
| 6970A – Resistance | 6970A – Reactance |
| 7300 | A7770A |
| 7782AA | OVL |
| iMotion 1 & 2 | AT400 |
| ECI |
| 895/1000 2000 | VFE2500 Voltage: 220VAC 115VAC (220 is default if no selection made) |
| Other |
| IPC Encore (closed loop) | Mitsubishi LV1/4K |
| Delco (closed loop) | Schindler QKS 14 & 15 |
| Atlantic/Vertisys Model: |
| Other (wiring diagram required): |
| Powered Freight Style Doors |
| Door Controller Model |
| Peelle | New | Existing |
| Model: | (electrical schematic required) |
| Courion | New | Existing |
| Model: | (electrical schematic required) |
| EMS | New | Existing |
| Model: | (electrical schematic required) |
| Other | New | Existing |
| Model: | (electrical schematic required) |
| Door Operation (freight only) |
| Opening: | Automatic | Momentary pressure |
| Closing: | Automatic | Momentary pressure |
|  |  | Constant pressure |
| Fire Ph. l Closing: | Automatic | Momentary pressure |
|  |  | Constant pressure |

Serial Link (Fixtures must be 24VDC, 6 watts max)

Car Operating Panel Hall Calls # of risers: Call pushbuttons must be mechanical.

Serial fixture boards to be sent to fixture manufacturer / contractor for pre-wire? Yes (If so, indicate where below) No Ship serial boards to: C.E. Electronics EPCO Dupar Innovation Industries Monitor MAD ERM PTL Elevator Contractor Office Please indicate Contact Person / Number in Special Notes below Which boards to be sent? COP Hall Station

Auxiliary Car Station

Hand-held programming unit (optional, needs Serial COP) Number of units:

Car Calls Voltage: 24 48 120 Other: AC DC Type: LED Incandescent

Hall Calls Voltage: 24 48 120 Other: AC DC Type: LED Incandescent

Position Indicators

Car MCE CE 3-wire driver board (built into controller) MCE E-Motive 3-wire driver board (built into controller) MAD OR Other [Customer-supplied Serial Device] (discrete signals from MCE only – fill in *Discrete section below) *Discrete signals (Multi-Light, serial, or non-serial digital) *Provide information below: Voltage: 24 48 120 Other: AC +DC -DC Type: Multi-light To customer-supplied external serial driver board Brand: Model: Driver Location(s): One line per floor Binary code begins at landing 1 00 01

Hall Location: All floors Main fire return Other: MCE CE 3-wire driver board (built into controller) MCE E-Motive 3-wire driver board (built into controller) MAD OR Other [Customer-supplied Serial Device] (discrete signals from MCE only – fill in *Discrete section below) *Discrete signals (Multi-Light serial, or non-serial digital) *Provide information below: Voltage: 24 48 120 Other: AC +DC -DC Type: Multi-light To customer-supplied external serial driver board Brand: Model: Driver Location(s): One line per floor Binary code begins at landing 1 00 01

Voice annunciation MCE CE 3-wire driver board interface (built into controller) Other:

Special Notes:

| Lanterns |
| --- |
| Car lanterns MCE CE 3-wire driver board (built into controller) MCE E-Motive 3-wire driver board (built into controller) Discrete signals – Bulb wattage Voltage: 24 48 120 Other: AC DC Type: Chime Gong |
| Hall Lanterns MCE CE 3-wire driver board (built into controller) MCE E-Motive 3-wire driver board (built into controller) Discrete signals – Bulb wattage Voltage: 24 48 120 Other: AC DC Type: Chime Gong |
| Passing floor signal MCE CE 3-wire driver board (built into controller) MCE E-Motive 3-wire driver board (built into controller) Discrete signals Voltage: 24 48 120 Other: AC DC Type: Chime Gong Passing floor enable (“S” button) |
| Status Indicators |
| Type | Volts | AC | DC |
| Attendant Light | 24 48 120 Other: |  |  |
| Attendant Buzzer | 24 48 120 Other: |  |  |
| Call Registration Buzzer | 24 48 120 Other: |  |  |
| Door Closing Buzzer (typically freight only) | 24 48 120 Other: |  |  |
| Door Hold Light | 24 48 120 Other: |  |  |
| Door Left Open Bell | 24 48 120 Other: |  |  |
| EMT Service Light, Car | 24 48 120 Other: |  |  |
| EMT Service Light, Hall | 24 48 120 Other: |  |  |
| Fire Light | 24 48 120 Other: |  |  |
| Fire Buzzer | 24 48 120 Other: |  |  |
| Hospital Light | 24 48 120 Other: |  |  |
| Hospital Buzzer | 24 48 120 Other: |  |  |
| In-Service Light | 24 48 120 Other: |  |  |
| In-Use Light | 24 48 120 Other: |  |  |
| Load Status Light | 24 48 120 Other: |  |  |
| Nudging Buzzer | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |
|  | 24 48 120 Other: |  |  |

| Floor Label* | Landing # | Floor Height | Car | Car | Car | Car |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | F | R | F | R | F | R | F | R |
|  | overhead 15-16 14-15 13-14 12-13 11-12 10-11 9-10 8-9 7-8 6-7 5-6 4-5 3-4 2-3 1-2 Pit | Check front and rear floor openings below |
|  | 16 |  |  |  |  |  |  |  |  |  |
|  | 15 |  |  |  |  |  |  |  |  |  |
|  | 14 |  |  |  |  |  |  |  |  |  |
|  | 13 |  |  |  |  |  |  |  |  |  |
|  | 12 |  |  |  |  |  |  |  |  |  |
|  | 11 |  |  |  |  |  |  |  |  |  |
|  | 10 |  |  |  |  |  |  |  |  |  |
|  | 9 |  |  |  |  |  |  |  |  |  |
|  | 8 |  |  |  |  |  |  |  |  |  |
|  | 7 |  |  |  |  |  |  |  |  |  |
|  | 6 |  |  |  |  |  |  |  |  |  |
|  | 5 |  |  |  |  |  |  |  |  |  |
|  | 4 |  |  |  |  |  |  |  |  |  |
|  | 3 |  |  |  |  |  |  |  |  |  |
|  | 2 |  |  |  |  |  |  |  |  |  |
|  | 1 |  |  |  |  |  |  |  |  |  |
| Capacity: lbs kg |  |  |  |  |
| Up Speed: fpm m/s |  |  |  |  |
| Down Speed: fpm m/s |  |  |  |  |
| Total Travel: ft m |  |  |  |  |

### * Floor Label note: If using CE or E-Motive driver board, floor label should not be more characters than the number of digital PI
   display characters ()

### Hoistway NEMA Rating:    1 (standard)       12       4      4X

Number of Hoistways:

EECO Hoistway Limit Switches (Note: Only two mechanical limit switches are required with LS-EDGE landing system)

MCE Landing System:

Tape (LS-EDGE)    Tape length         Tape Type:   Steel (Std.)   Stainless Steel

Tape (LS-QUTE) Hoistway NEMA 1 only    Tape length         Tape Type:   Steel (Std.)   Stainless Steel

Vane (LS-STAN)

Rail (lbs):      8 – 12       15 – 18.5        22.5 – 30

Customer Supplied Landing System

Traveling Cable  (Note: Separate form required)

# Text boxes

Logistics Information

In order to better serve you and meet your schedule, this form must be completed and signed. Timely delivery and trouble-free installation begin with this data form. Accurate and complete information is essential. Non-response to a question will be defined as meaning that the item does not apply.

Logistics & Code Data

Control Information

General & Hydraulic Data

Door Information

Fixtures

Landings & Openings